## Slide 1
CLOUD
IoT
5G / 6G
IP Architecture
Across Modern Networks
How one protocol connects Cloud infrastructure,
IoT devices and 5G/6G mobile networks
Dimitrios Dalaklidis | Network Design | University of Western Macedonia

## Slide 2
Section 1: IP in Cloud Infrastructure
IP is the universal layer that makes dynamic, virtualised cloud environments possible.
VMs & Containers
Each VM or container gets its own virtual network interface and IP address — creating the illusion of an independent compute node. IP acts as the common layer connecting virtual workloads to physical infrastructure.
Virtual Switches & Routers
Virtual switches forward IP packets between VMs on the same physical host without touching the physical network — delivering low latency. Virtual routers connect isolated tenant networks and provide external access.
VXLAN Overlay Networks
VXLAN encapsulates Ethernet frames inside IP/UDP packets, enabling up to 16 million isolated virtual networks to coexist on the same physical Layer 3 fabric — each tenant identified by a unique VNI.
Hardware impact
Modern NICs offload IP checksum calculation and VXLAN encapsulation from the CPU — critical at scale. Multiqueue NICs allow parallel processing of multiple IP flows, sustaining performance in high-density VM environments.

## Slide 3
Section 2: IP in IoT — Constrained Devices
Running IP on devices with kilobytes of RAM required fundamental protocol redesign — not just optimisation.
IoT Node Classes (RFC 7228)
C0
< 10 KiB
Cannot run IP stack — requires gateway proxy
C1
~10 KiB
Needs 6LoWPAN + lightweight stack (uIP/lwIP)
C2
~50 KiB
Can run full protocols — with energy constraints
IPv6 — Essential for IoT Scale
IPv4's 4 billion addresses are exhausted. IPv6 provides 340 undecillion addresses, stateless autoconfiguration, and simpler headers — critical for billions of connected devices.
6LoWPAN — Header Compression
Compresses IPv6 headers from 40 bytes to just 2–3 bytes. Essential for IEEE 802.15.4 networks with 127-byte frame limits and severe bandwidth constraints.
Lightweight OS Stacks
Contiki and RIOT implement event-driven TCP/IP with minimal footprint, enabling real-time IP communication on hardware with less RAM than a 1980s home computer.
Design trade-off: Every IoT stack choice balances IP compatibility, energy consumption, and memory footprint.

## Slide 4
Section 3: IP in 5G/6G Networks
5G is built all-IP from the ground up — every packet, every control signal, every voice call travels over IP.
All-IP Architecture
Voice, data and control signals converge on IP — eliminating legacy circuit-switched infrastructure. This simplifies network management and enables full convergence between fixed and mobile networks.
Mobility & Handover
Proxy Mobile IPv6 (PMIPv6) keeps a user's IP address constant across base stations. Session and Service Continuity (SSC) modes deliver zero-interruption handovers — even at high speed.
Network Slicing (SRv6)
IP-in-IP encapsulation and Segment Routing (SRv6) carve the same physical infrastructure into isolated virtual networks — each with its own QoS profile for autonomous vehicles, video streaming, or smart grids.
URLLC & Edge Computing
Ultra-Reliable Low Latency Communications demand sub-1ms IP stacks. Multi-access Edge Computing (MEC) pushes processing to the network edge using SmartNICs and IP-aware routing — avoiding central datacenter round-trips.
6G evolution: IP is being extended to support semantic communication — where the meaning of data influences routing decisions, not just destination addresses.

## Slide 5
IP Across Domains — At a Glance
CLOUD
IoT
5G / 6G
Scale
Millions of VMs
& containers
Billions of
constrained nodes
Billions of
mobile users
Key tech
VXLAN, overlay
networks
6LoWPAN, IPv6
compression
SRv6, PMIPv6
MEC
Main challenge
Isolation &
scalability
Energy &
memory
Latency &
mobility
IP role
Routing between
virtual entities
Universal address
for tiny devices
All-IP convergence
& slicing

## Slide 6
CONCLUSION
IP: The Common
Language of Modern Networks
In Cloud, IP enables millions of virtual entities to communicate as if on a single flat network — while staying physically isolated through VXLAN and overlay techniques.
In IoT, IPv6 and 6LoWPAN make IP viable on devices with kilobytes of RAM — extending internet connectivity to billions of constrained sensors and actuators.
In 5G/6G, an all-IP architecture converges voice, data and control into one fabric — with network slicing and edge computing delivering ultra-low latency at scale.
References: RFC 7348 (VXLAN) · RFC 7228 (IoT Nodes) · Mulligan 2007 (6LoWPAN) · Shayea et al. 2020 (5G Mobility)